## Slide 1
Experiment No. 3
Preparation and standardization of approximately 0.1N acetic acid solution (CH3COOH) by using standardized sodium hydroxide (NaOH)

## Slide 2
Acetic acid (CH3COOH) also known as ethanoic acid, (Ka = 1.8 × 10-5 at 25 ◦C) and partially dissociated in an aqueous solution.
Glacial acetic acid is a pure and water-free acetic acid. It is a colorless liquid that absorbs water from the environment (hygroscopic), and freeze at 16.5 ◦C to a colorless crystalline solid.
Acetic acid can be detected by its characteristic smell which has a distinctive pungent odour.

## Slide 3
Concentrated acetic acid is corrosive and therefore must be handled with appropriate care, since it can cause skin burns and permanent eye damage. These burns may not appear until hours after exposure.
The titration of CH3COOH against NaOH solution is a titration of weak acid against strong base.

## Slide 4
The solution at equivalence point not neutral, but slightly alkaline, the calculated pH at equivalence point is 8.72.
In this experiment, methyl orange or methyl red cannot be used because they change their color at a much lower pH (acidic medium), i.e. the color is changed before the equivalence point. Therefore, phenolphthalein (ph.ph) is used as indicator because its color changes in the alkaline region at a pH range of (8-9.6).
Preparation of solutions:
1- Prepare 0.1 N NaOH in 250 mL of distilled water.
2- Prepare approximately 0.1 N CH3COOH in 250 mL of distilled water.

## Slide 5
Prepare approximately 0.1 N CH3COOH in 250 mL of distilled water.
Sp.gr = 1.049 , % = 98% , Formula weight = 60 g/mole.
≈ 1.5 mL
You must take 1.5 ml of concentrated CH3COOH with a pipet, and dilute to 250 ml with distilled water in a 250ml-volumetric flask to obtain approximately 0.1 N CH3COOH.

## Slide 6
V CH3COOH (ml) | V NaOH (ml)
5 | V1
5 | V2
5 | V3
Procedure:
1. Pipet 5 ml of acetic acid solution into a conical flask.
2. Add 2-3 drops of phenolphthalein indicator. The solution will be colorless.
3. Titrate the solution with the standardized NaOH solution from the burette until the color of solution changes into pink. Repeat the titration three (3) times.